## Slide 1: Fault Tolerant Flight Control

## Slide 2: Specify System
Intent: In order to increase reliability of the Control System and help reduce the workload of the Flight Crew in high stress situations resulting from various failure modes, a fault tolerant flight system shall be integrated.

## Slide 3: Specify System
REQ1: The system shall provide fault-tolerant flight control by maintaining aircraft stability and command execution in the presence of multiple unexpected failure types, including actuator jams, reduced control effectiveness, structural failures, aerodynamic changes, and sensor noise.

## Slide 4: Specify System
REQ2: The system shall utilize a model-free, Deep Reinforcement Learning-based (Soft Actor-Critic) control architecture for both attitude and altitude control.
REQ3: The system shall implement a cascaded controller structure, where an inner-loop controller manages attitude (pitch, roll, sideslip) and an outer-loop controller manages altitude tracking.
REQ4: The system shall deliver robust flight performance under varying initial flight conditions, reference signal shapes, biased sensor noise, and atmospheric disturbances.
REQ5: The system shall operate at a refresh rate of at least 100 Hz, generating smooth incremental control commands to the aircraft’s elevator, aileron, and rudder.
REQ6: The system shall interface with existing aircraft navigation and auto-throttle systems, commanding only control surfaces while leaving airspeed control to external systems.
REQ7: The system shall be trained offline on nominal aircraft dynamics and demonstrate robust, adaptive response to failures during online operation without the need for parameter retuning or retraining.
REQ8: The system shall generalize its control policy to untrained scenarios, adapting to unmodeled disturbances and maintaining performance without explicit reconfiguration.

## Slide 5: Specify System
Users:
  On board flight control computer/autopilot:
    executes algorithm
  Flight crew:
    Receives stable aircraft and can interact with cockpit control
  Maintenance and health management engineers:
    Analyse logs

## Slide 6: Specify System
  Inputs
    Aircraft state vector:
      p,q,r,V, alpha, beta, theta, phi, chi, h
    Control surface positions: elevator, rudder, aileron
    Guidance reference: h, theta, phi, beta
    Context data: Fault flags etc.
  Outputs
    Inner loop attitude controller: delta(elevator, rudder,aileron)
    Outer loop altitude controller: delta theta
    Supervisory/ status channel:

## Slide 7: Specify System
ML Constituents

## Slide 8: Specify System
ML Constituents
Algorithm: Soft Actor-Critic (SAC)
Policy: Multivariate Gaussian with tanh squashing for bounded control
Training: Offline on non-failed dynamics using high-fidelity simulation data
Inputs: Weighted error vectors, angular rates, current control input
Outputs: Control surface deflection increments or pitch angle reference

## Slide 9: Specify System
OD: The operational domain is real-time, closed-loop flight control of a jet aircraft, during all phases of normal flight, under both nominal and multiple severe failure/disturbance scenarios, at a 100 Hz rate, using only control surface commands—validated in high-fidelity simulation, and intended for experimental research aircraft.

## Slide 10: Specify System
Domain Aspect | Scope/Limitations
Aircraft | CS-25 jet, Cessna Citation 500/PH-LAB, clean configuration
Flight Envelope | 2,000–5,000 m altitude; 90–140 m/s speed; typical maneuvers
Failures | Single surface jam, reduced effectiveness, icing, c.g. shift
Disturbances | Sensor noise/bias, discrete gusts (not severe/extreme weather)
Control Surfaces | Elevator, aileron, rudder (no throttle control)
Sensor Assumptions | Realistic noise/bias, no total sensor loss
Update Rate | 100 Hz real-time
Excluded | Severe failures, post-stall, engine-out, extreme environments